# 豬糞尿處理水及不同乾水距對地表逕流水質之影響
# 謝 昭 賢
畜產試驗所
本試驗利用模擬降雨來評估施灌豬糞尿處理水及不同乾水距對地表逕流水質之影響。本試驗以4×3複因子設計，試驗因子為豬糞尿處理水因子 (含固液分離水、厭氣水、排放水及對照組四種處理) 及乾水距因子 (含施灌豬糞尿處理水後第1、第4及第14天產生逕流)。共12個填滿砂質粘壤土之土箱。本試驗在降雨強度50 mm/hr之模擬降雨下，俟產生逕流後，持續進行30 min之降雨延時，所得之逕流資料用以分析逕流中之TKN、NH3-N、NO3--N、TP、DP及EC。結果顯示：施灌豬糞尿處理水會顯著地影響逕流之水質，且逕流水之濃度與豬糞尿處理水之種類而有所不同，其中以施灌固液分離水之地表逕流水濃度最高，厭氣水次之，但每公頃之流失量均很低；在施灌豬糞處理水後，第1天發生暴雨之逕流水濃度顯著地高於第4及第14天之逕流水質。
關鍵字：逕流、處理水、水質

RUNOFF QUALITY FROM SOIL BINS RECEIVING EFFLUENTS OF THE TREATED SWINE WASTEWATER
# C. H. Hsieh
Taiwan Livestock Research Institute
A small-scale of rainfall simulator with a 50 mm/hr of rainfall intensity and a 30 min of rainfall duration was used to evaluate the runoff quality from soil bins receiving effluents of the treated swine wastewater. The 4×3 factorial experiment design was employed. Two factors consisted of types of effluent with four treatments (solid-liquid separation effluent, anaerobic effluent, aerobic effluent and control), and drying interval with three treatments (rainfall was simulated at the first, fourth and fourteenth day after applying the effluents). The results showed that runoff quality from solid-liquid separation effluent was the worst in the treated swine wastewater, and from the first day after applying effluent was also the worst among the three drying interval treatments. However, the percentage of mass loss from applying the treated swine wastewater by surface runoff was small.
Key words: Runoff, Wastewater, Water quality